## Slide 1: Ratiometric Sensor Analysis
What is a ratiometric sensor?
Why does this effect need to be removed from the measured data?
Analysis options (there may be more)
  Plot VOUT/ VDDM vs x/ VDDDS
  Plot VOUT vs x
  Plot VOUT/ VDDM vs x
  Plot VOUT*(VDDDS / VDDM) vs x

## Slide 2: Ratiometric Sensors
A ratiometric sensor’s output is dependent on two factors
  The first factor is the desired variable that we are trying to measure
    Position, pressure, etc.
  The second factor is a reference or supply voltage
    This effect is not desired and must be compensated for in the data analysis to determine the static sensitivity and offset due to the desired variable

## Slide 3: Examples of Ratiometric Sensors
Wheatstone bridge
Accelerometer
Gauge pressure sensor

## Slide 4: General Equation for the Transfer Function of a Ratiometric Sensor
Where:
y is the sensor’s output (typically a voltage, Vout)
m is the sensor’s static sensitivity
x is the sensor’s input variable (pressure, etc.)
b is the sensor’s output offset (typically a voltage, Voff)
VDDM is the measured (actual) supply voltage
VDDDS is the data sheet (ideal) supply voltage

## Slide 5: The Goal
Often we want to determine m and b from measured data
  Measure y as x is varied
We then compare our measured values for m and b to the data sheet values
  Verify the sensor’s accuracy
  Compare with % error calculations

## Slide 6: The Problem
If VDDM is identical to VDDDS then there is no issue, as y then only depends on m and b
  Can then find m and b from a plot of y vs. x and compare directly to data sheet values
But, typically VDDM is NOT identical to VDDDS
So, need to compensate for VDDM ≠ VDDDS

## Slide 7: Ideal Sensor Response Example
Static sensitivity (slope) = 0.50 V/(x units)
Offset (y-intercept) = 2.5V
VDDM = VDDDS = 5.0V
Chart: Ideal Response
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5

## Slide 8: Method #1
Plot y/VDDM vs. x/VDDDS
Compare the resulting slope directly to the data sheet value for the sensor’s static sensitivity
But, the offset value needs to be multiplied by VDDDS before comparing to the data sheet value

## Slide 9: Method #1
VDDM = 5.1V VDDDS = 5.0V
Compare the resulting slope directly to the data sheet value for the sensor’s static sensitivity
  0.50 = 0.50
But, the offset value needs to be multiplied by VDDDS before comparing to the data sheet value
  2.5V = 0.50 * 5.0V = 2.5V
Plot y/VDDM vs. x/VDDDS
Chart: Method #1
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2
 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5
.
.

## Slide 10: Method #2
Plot y vs. x
Compare the resulting slope to the data sheet value for the sensor’s static sensitivity multiplied by VDDM /VDDDS
Compare the resulting offset to the data sheet value for the sensor’s offset multiplied by VDDM /VDDDS

## Slide 11: Method #2
VDDM = 5.1V VDDDS = 5.0V
Compare the resulting slope to the data sheet value for the sensor’s static sensitivity multiplied by VDDM /VDDDS
  0.51 = 0.50 * (5.1V/5.0V) = 0.51
Compare the resulting offset to the data sheet value for the sensor’s offset multiplied by VDDM /VDDDS
  2.55V = 2.5V * (5.1V/5.0V) = 2.55V
Plot y vs. x
Chart: Method #2
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 2.55 | 3.06 | 3.57 | 4.08 | 4.59 | 5.1 | 5.61 | 6.12 | 6.63 | 7.14 | 7.65
.
.

## Slide 12: Method #3
Plot y/VDDM vs. x
Compare the resulting slope to the data sheet value for the sensor’s static sensitivity divided by VDDDS
Compare the resulting offset to the data sheet value for the sensor’s offset divided by VDDDS

## Slide 13: Method #3
VDDM = 5.1V VDDDS = 5.0V
Compare the resulting slope to the data sheet value for the sensor’s static sensitivity divided by VDDDS
  0.10 = 0.50 / 5.0V = 0.10
Compare the resulting offset to the data sheet value for the sensor’s offset divided by VDDDS
  0.50 = 2.50V / 5.0V = 0.50
Plot y/VDDM vs. x
Chart: Method #3
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5
.
.

## Slide 14: Method #4
Plot y*VDDDS /VDDM vs. x
Compare the resulting slope directly to the data sheet value for the sensor’s static sensitivity
Compare the resulting offset directly to the data sheet value for the sensor’s offset

## Slide 15: Method #4
VDDM = 5.1V VDDDS = 5.0V
Compare the resulting slope directly to the data sheet value for the sensor’s static sensitivity
  0.50 = 0.50
Compare the resulting offset directly to the data sheet value for the sensor’s offset
  2.50V = 2.5V
Plot y*VDDDS /VDDM vs. x
Chart: Method #4
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5
.
.
Note that the slope and offset are the same as for the ideal example!

## Slide 16: Which Method is Best?
All “work”, as they allow a comparison between the experimental (measured) and expected (data sheet) static sensitivity and offset
But, it is better to use a method that requires less manipulation of the data sheet values before the comparisons are made
  Any calculation errors will be more obvious
  Based on this criterion, prefer method #4 followed by method #3
For analysis in ME345W lab reports or homework submissions, use Method #4